## Slide 1
A brief overview: Minimum Ignition Energy Transition in Biogas Mixtures, and Droplet-Laden Turbulent Flows
V.S. Papapostolou, G. Ozel-Erol, C. Turquand d’Auzay, N. Chakraborty
School of Engineering, Newcastle University, UK
UKCTRF PhD Student Conference, 2020
16th September 2019
Online

## Slide 2
Motivation
1/11
Localised forced ignition (spark or laser) plays a dominant role in transportation and energy production
  Internal Combustion (IC) engines and Gas turbines
  Important from the point of view of accidental explosion and fire safety
Ignition not only initiates combustion but also influences subsequent burning
Biogas utilisation is a growing area of interest, particularly for developing countries
  Used as a fuel alternative for personal and light commercial vehicles
  However the efficiency and stability of biogas-fuelled engines are not as good as that obtained for the fuel for which the engine was originally designed to operate with
  Demand for both micro (personal) and macro (governmental and institutional) level applications

## Slide 3
Numerical Implementation
2/11
Compressible 3D DNS code SENGA+
Uniform Cartesian grid
All boundaries are considered to be non-reflecting, pointwise inflow-outflow
Initial turbulent field is generated by a pseudo-spectral method adhering to the Batchelor-Townsend Spectrum
Spatial differentiation – high order finite difference scheme
Time advancement – Explicit low-storage 3rd order Runge-Kutta scheme
Geometrical description of the domain
x
y
z
1 K.W. Jenkins, R.S. Cant, Proc. 2nd AFOSR Conference on DNS and LES (1999)
2 R.S. Rogallo, NASA Ames Research Centre (1990)
3 G.K. Batchelor and A.A. Townsend, Proceedings Royal Society London (1948)

## Slide 4
Numerical Implementation
3/11
Geometrical description of the domain
x
y
z
Three domain sizes used, dependent on the turbulence intensity, ), ) and ), where is the Zel’dovich flame thickness of the stoichiometric mixture
Cartesian grid of , and respectively, ensures:
  10 grid points across the thermal flame thickness
  where is the Kolmogorov length scale
Spark location is at the centre of the domain
Energy deposition accounted for by addition of source term to energy equation
Energy deposition duration () and width () kept constant, only spark power () is varied to find the MIE

## Slide 5
Numerical Implementation: Parameters investigated
4/11
To demonstrate and explain the influences of initial turbulence intensity () and level of dilution () on the Minimum Ignition Energy (MIE) of biogas-air mixtures.
MIE – the smallest amount of energy which can be deposited into the mixture for a successful ignition to occur
Biogas combustion has the following global reaction, with the Diluent being C to represent biogas:
Level of dilution () is defined following the definitions of Galmiche et al.
  In the unburned mixture:
  In the fuel:
4 Galmiche, B. et al., Effects of dilution on laminar burning velocity of premixed methane/air flames. Energy Fuels. 25(3), 948–954 (2011)

## Slide 6
Numerical Implementation: Parameters investigated
5/11
Four levels of dilution investigated:
Stoichiometric mixture in all cases:
Isotropic decaying turbulence, initial turbulence intensities : = [0 20]
Integral length scale () kept constant
Computational cost ~ 570 DNS cases at a cost of 5.85 core hours

## Slide 7
Numerical Implementation: Chemical Mechanism
6/11
Due to computational cost, a two-step chemical mechanism presented by Westbrook and Dryer has been used
Compromise between single-step chemistry and more complex mechanisms
Pre-exponential adjustment (PEA) proposed by Bibrzycki and Poinsot implemented
Validated for both and mixtures, against experimental results and other chemical mechanisms (2s_CM2and GRI-Mech 3.0 [43] and) and.
5 Westbrook, C.K., Dryer, F.L.: Simplified reaction mechanisms for the oxidation of hydrocarbon fuels in flames.. Combust. Sci. Technol.. 27 (1981).
6 Bibrzycki, J., Poinsot, T.: Reduced chemical kinetic mechanisms for methane combustion in O2/N2 and O2/CO2 atmosphere. CERFACS (2010).
7 Smith, G., Golden, D., Frenklach, M., Moriarty, N., Eiteneer, B., Goldenberg, M., Bowman, C., Hanson, R., Song, S., Gardiner, W., Lissianski, V., Qin, Z.,Gri-Mech 3.0. Accessed February 25. . , (2018).

## Slide 8
Results: Dilution effects on MIE
7/11
Normalised energy deposited by the spark:
  - is the MIE
  - indicate values sufficient just for thermal runaway/self-sustained flame propagation, respectively
  - indicates the dilution level
  - indicates laminar quiescent conditions

## Slide 9
Results: Dilution effects on MIE
7/11
Normalised energy deposited by the spark:
  - is the MIE
  - indicate values sufficient just for thermal runaway/self-sustained flame propagation, respectively
  - indicates the dilution level
  - indicates laminar quiescent conditions
  - Increases (left to right)
  content increases

## Slide 10
Results: Dilution effects on MIE
7/11
Normalised energy deposited by the spark:
  - is the MIE
  - indicate values sufficient just for thermal runaway/self-sustained flame propagation, respectively
  - indicates the dilution level
  - indicates laminar quiescent conditions
  - Increases (left to right)
  content increases
  MIE requirement increases

## Slide 11
Results: Dilution effects on MIE
7/11
Temporal evolutions of the maximum value of under laminar conditions with and as indicated by the legend for input energy equal to the MIE for under laminar conditions.
Non-dimensional temperature:
is the instantaneous dimensional temperature,
is the unburned gas temperature,
is the adiabatic flame temperature for the corresponding level of dilution

## Slide 12
Results: Dilution effects on MIE
7/11
Temporal evolutions of the maximum value of under laminar conditions with and as indicated by the legend for input energy equal to the MIE for under laminar conditions.
Non-dimensional temperature:
is the instantaneous dimensional temperature,
is the unburned gas temperature,
is the adiabatic flame temperature for the corresponding level of dilution
= 3.55
Laminar cases

## Slide 13
Results: Dilution effects on MIE
7/11
Temporal evolutions of the maximum value of under laminar conditions with and as indicated by the legend for input energy equal to the MIE for under laminar conditions.
Non-dimensional temperature:
is the instantaneous dimensional temperature,
is the unburned gas temperature,
is the adiabatic flame temperature for the corresponding level of dilution
= 3.55
Laminar cases
= 0, 0.025
>

## Slide 14
Results: Dilution effects on MIE
7/11
Temporal evolutions of the maximum value of under laminar conditions with and as indicated by the legend for input energy equal to the MIE for under laminar conditions.
Non-dimensional temperature:
is the instantaneous dimensional temperature,
is the unburned gas temperature,
is the adiabatic flame temperature for the corresponding level of dilution
= 3.55
Laminar cases
= 0, 0.025
>
= 0.05, 0.1
<

## Slide 15
Results: MIE transition & Characterisation
8/11
Variation of the normalised MIEs with for different dilution levels .
MIE Transition – the drastic increase of the MIE requirement past a critical turbulence intensity
  Gradual increase, small MIE
  Drastic increase, large MIE

## Slide 16
Results: MIE transition & Characterisation
8/11
Variation of the normalised MIEs with for different dilution levels .
Self similar profiles obtained for all values
In agreement with experimental results
Same behaviour observed for droplet laden mixtures╪
╪ Vassilios Papapostolou , Gulcan Ozel Erol , Charles Turquand d’Auzay & Nilanjan Chakraborty (2020): A Numerical Investigation of the Minimum Ignition Energy Requirement for Forced Ignition of Turbulent Droplet-laden Mixtures, Combustion Science and Technology

## Slide 17
Results: MIE transition & Characterisation
9/11
Variation of the normalised MIEs with for different dilution levels .

## Slide 18
Results: MIE transition & Characterisation
9/11
8 Shy, S.S., Liu, C.C., Shih, W.: Ignition transition in turbulent premixed combustion. Combust. Flame. 157 (2), 341–350 (2010).
9 Cardin, C., et al.: Experimental analysis of laser-induced spark ignition of lean turbulent premixed flames: new insights Comb. Flame. 160 (8), 1414–1427 (2013).
10 Turquand d’Auzay, C., et al.: On the minimum ignition energy and its transition in the localised forced ignition of turbulent homogeneous mixtures. Comb. Flame.201, 104–117 (2019).

## Slide 19
Results: MIE transition & Characterisation
10/11

## Slide 20
Results: MIE transition & Characterisation
10/11
,
Heat release must overcome the overall heat transfer rate
MIE transition attributed to bending effect
varies linearly (i.e. ) with small turbulence intensities
becomes less sensitive to the changes in with .

## Slide 21
Results: MIE transition & Characterisation
10/11
8 Shy, S.S., Liu, C.C., Shih, W.: Ignition transition in turbulent premixed combustion. Combust. Flame. 157 (2), 341–350 (2010).
9 Cardin, C., et al.: Experimental analysis of laser-induced spark ignition of lean turbulent premixed flames: new insights Comb. Flame. 160 (8), 1414–1427 (2013).
10 Turquand d’Auzay, C., et al.: On the minimum ignition energy and its transition in the localised forced ignition of turbulent homogeneous mixtures. Comb. Flame.201, 104–117 (2019).

## Slide 22
Conlusions
The MIE of stoichiometric biogas-air mixtures with varying levels of dilution have been numerically evaluated under homogeneous isotropic decaying turbulence for a wide range of initial turbulence intensities using three-dimensional DNS.:
The MIE for uniformly dispersed mono-sized n-heptane droplet-laden mixtures under homogeneous isotropic decaying turbulence has been numerically evaluated for a range of different initial turbulence intensities, droplet diameters and overall equivalence ratios, following similar methodology to that described above for the biogas.
11/11

## Slide 23
Conclusions
Good agreement with existing experimental results
11/11

## Slide 24
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
11/11

## Slide 25
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
Scaling analysis and flame wrinkling statistics explained the power law nature of MIE transition. The power law exponent was not significantly affected by the presence and level of dilution.
11/11

## Slide 26
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
Scaling analysis and flame wrinkling statistics explained the power law nature of MIE transition. The power law exponent was not significantly affected by the presence and level of dilution.
Stochasticity of the ignition and flame propagation events for the MIE values explained in terms of the competition between the heat release and thermal diffusion rates. Same behaviour was observed for droplet laden mixtures as well.
11/11

## Slide 27
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
Scaling analysis and flame wrinkling statistics explained the power law nature of MIE transition. The power law exponent was not significantly affected by the presence and level of dilution.
Stochasticity of the ignition and flame propagation events for the MIE values explained in terms of the competition between the heat release and thermal diffusion rates. Same behaviour was observed for droplet laden mixtures as well.
First order effect: initial turbulence intensity
11/11

## Slide 28
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
Scaling analysis and flame wrinkling statistics explained the power law nature of MIE transition. The power law exponent was not significantly affected by the presence and level of dilution.
Stochasticity of the ignition and flame propagation events for the MIE values explained in terms of the competition between the heat release and thermal diffusion rates. Same behaviour was observed for droplet laden mixtures as well.
First order effect: initial turbulence intensity
Increase :
      Increases the MIE demand
      Decreases critical turbulence intensity
11/11

## Slide 29
Conclusions
Good agreement with existing experimental results
MIE transition observed for all levels of , and for droplet laden mixtures
Scaling analysis and flame wrinkling statistics explained the power law nature of MIE transition. The power law exponent was not significantly affected by the presence and level of dilution.
Stochasticity of the ignition and flame propagation events for the MIE values explained in terms of the competition between the heat release and thermal diffusion rates. Same behaviour was observed for droplet laden mixtures as well.
First order effect: initial turbulence intensity
Increase :
      Increases the MIE demand
      Decreases critical turbulence intensity
11/11
Increase of initial droplet diameter
Decrease of initial global equivalence ratio

## Slide 30
Thank you for your time and attention
The financial support of British Council, EPSRC, and the computational support of Rocket, Cirrus and ARCHER are gratefully acknowledged.
Questions ?
V.Papapostolou et al. (2020): A Numerical Investigation of the Minimum Ignition Energy Requirement for Forced Ignition of Turbulent Droplet-laden Mixtures, Combustion Science and Technology
V.Papapostolou et al. (2020): A numerical investigation of the effects of fuel composition on the minimum ignition energy for homogeneous biogas-air mixtures, Flow, Turbulence and Combustion (under review currently)
Droplet-laden Mixtures
Combustion Science and Technology

## Slide 31
Results: MIE transition & Characterisation
heat release must overcome the overall heat transfer rate
  Scales as:
    is the flame surface area to volume ratio
    is the heat of combustion
    is the actual flamelet area
    is the projected flame surface
Which also scales as:
  is the effective diffusive thermal flux
  Scales as:
    is the eddy diffusivity
    Turbulent diffusion >> than the molecular diffusion rate
    is the critical radius of the hot gas kernel
    for self-sustained propagation
  By substituting
  is by definition is the wrinkling factor
)
    For a certain - and constants

## Slide 32
Results: MIE transition & Characterisation
12/13
8 Shy, S.S., Liu, C.C., Shih, W.: Ignition transition in turbulent premixed combustion. Combust. Flame. 157 (2), 341–350 (2010).
9 Cardin, C., et al.: Experimental analysis of laser-induced spark ignition of lean turbulent premixed flames: new insights Comb. Flame. 160 (8), 1414–1427 (2013).
10 Turquand d’Auzay, C., et al.: On the minimum ignition energy and its transition in the localised forced ignition of turbulent homogeneous mixtures. Comb. Flame.201, 104–117 (2019).
For
  is consistent with small values of for small turbulence intensities
  yields for large values of
  is the actual flamelet area
  is the projected flame surface
  is by definition is the wrinkling factor

## Slide 33
Results: Existing Findings

## Slide 34
MIE – Probabilistic Variable
Ignition is a stochastic phenomenon. MIE is determined as a probabilistic variable.
Experimentally it is determined by:
  First estimate the amount of energy to achieve more than 0% probability of successful ignition, and then the energy required to achieve 100% ignition.
  Numerous experimental realisations required, to ascertain ‘upper’ and ‘lower’ limits.
  Then the energy which leads to 50% ignition probability is taken to be the MIE.
  Experimental methodology cannot be followed using DNS due to the associated computational cost.
Fig. R1.1: Number of recordings as a function of deposited energy (energy classes of 0.2mJ wide) methane-air flame, , . Figure taken from Cardin et al. [1].

## Slide 35
MIE – Probabilistic Variable
Computationally the MIE is determined by:
  Increasing the amount of energy to achieve more than 0% probability of successful ignition whilst the turbulent realisation is unaltered.
  The MIE value obtained corresponds to a non-zero ignition probability as a successful event has occurred.
  Two further turbulent realisations are considered.
  A successful event was observed for one of these two, and an unsuccessful event for the other realisation
  Thus the reported MIE value corresponds to the ignition probability greater than 0% and smaller than 100%.
Fig. 2: Ignition probability as a function of the deposited energy (energy classes of 0.2mJ wide) methane-air flame, , . Linear fit applied to determine the MIE (3.750.1 mJ). Figure taken from Cardin et al. [1].

## Slide 36
Results: Flame-turbulence interaction
15/16
Figure 8. Number of successful events out of three different turbulent realisations (S01, S02, S03) across selected turbulent cases for and for the input ignition energy corresponding to .

## Slide 37
Results: Ignition/Propagation Definitions
11/13
Simulations carried out to evaluate the MIE for both Ignition and Propagation
  Successful Ignition - refers to a situation where surpasses at any point in time. If does not reach , it is referred to as a misfire. Simulations run until a successful ignition is observed ().
  Successful Propagation – obtained when the flame kernel burns without the aid of the ignitor after a successful ignition. It is determined by evaluating the temporal evolution of the burned gas volume, and if its temporal derivative is positive at , a successful self sustained propagation is obtained, otherwise it is considered to be quenched. (Comparable to experiments)

## Slide 38
Mathematical Background
3/13
Gaseous Phase:
Eulerian Approach is used to solve for gas phase combustion.
Addition of a source term to the energy equation to account for the energy deposition by the spark
The source term (spark energy) follows a Gaussian profile
-Total ignition energy input parameter
- Characteristic width parameter
- Energy deposition duration parameter

## Slide 39
Results: MIE transition & Characterisation
12/13
8 Shy, S.S., Liu, C.C., Shih, W.: Ignition transition in turbulent premixed combustion. Combust. Flame. 157 (2), 341–350 (2010).
9 Cardin, C., et al.: Experimental analysis of laser-induced spark ignition of lean turbulent premixed flames: new insights Comb. Flame. 160 (8), 1414–1427 (2013).
10 Turquand d’Auzay, C., et al.: On the minimum ignition energy and its transition in the localised forced ignition of turbulent homogeneous mixtures. Comb. Flame.201, 104–117 (2019).
Heat release must overcome the overall heat transfer rate
MIE transition attributed to bending effect
varies linearly (i.e. ) with small turbulence intensities
becomes less sensitive to the changes in with .
For
  is the actual flamelet area
  is the projected flame surface
  is by definition is the wrinkling factor

## Slide 40
Contents
1. Motivation
2. Mathematical Background and Numerical Implementation
1/13
3. Results
4. Conclusions