## Slide 1: Soot emissions prediction in aero-engine combustors using Incompletely Stirred Reactor Network modelling
Savvas Gkantonas*, Andrea Giusti**, Epaminondas Mastorakos*
16 Sept 2020
* University of Cambridge, UK
** Imperial College London, UK
UKCRTF meeting
Contact/Presenter: Savvas Gkantonas
(sg834@cam.ac.uk)

## Slide 2: Introduction
Soot emissions are a threat [1]
We need methodologies for the soot particle size distribution (PSD) [2]
Predicting soot is very hard even in laminar flames [2]
CFD approaches are required but are expensive
Cambridge Rich-Quench-Lean (RQL) burner [3]
0% dilution
40% dilution
[1] D’Anna, A. (2009). Proc. Comb. Inst. 32, 593–613.
[2] Rigopoulos, S. (2019). Flow Turbulence Combust. 103, 565–604.
[3] Gkantonas, S., Sirignano, M., Giusti, A., D’Anna, A., Mastorakos, E. (2020). Fuel 270, 117483.
Cost: O(106) CPUh

## Slide 3: Motivation and Objectives
Motivation
Develop inexpensive approaches:
Test many chemical schemes and soot models
Model many geometries and combustors
Provide estimates of soot emission and the exit PSD
Specific objectives
Develop an efficient Incompletely Stirred Reactor Network (ISRN) approach to post-process CFD simulations
Demonstrate efficiency and accuracy on model aero-engine combustors

## Slide 4: Incompletely Stirred Reactor (ISR) theory
Generalisation of the PSR (WSR)
Based on the Conditional Moment Closure (CMC) combustion model
ISR
stream 1 (e.g. fuel)
stream 2 (e.g. air)
core
outlet
inlet
V
mixture fraction
[1] N.S.A. Smith. PhD thesis, University of Sydney (1994).
[2] Klimenko, A.Y., Bilger, R.W. (1999). Prog. Energy Combust. Sci. 25
[3] Mobini, K., Bilger, R.W. (2004). Combust. Sci. Technol. 176.
Can be used as a post-processing step [1-3]

## Slide 5: Extension to a network approach
Conditional soot related quantities show strong spatial dependence
Cover the combustor with many interconnected ISRs  ISRN
Point 1
Point 2
Example of predicted soot conditional quantities (Cambridge RQL burner, C2H4, two-equation soot model)
ISRN equation:
inlets (advection)
source
micro-mixing
turbulent flux
1st order
modelling
CFD

## Slide 6: ISRN solution strategy
CFD input
Averaging
ISR spacing
Find ISRN quantities
ISRN solver
Results
Decoupled flow & ISRN
Example from Cambridge RQL
PSD prediction at exit
Model A
Model B
FDF-based data transfer
QUENCH
LEAN
RICH
ISR
ISR
ISR
ISR
ISR
ISR
ISR
ISR
ISR
ISR
ISR
ISR
Preprocessing
Various soot formation/oxidation rates

## Slide 7: Computational cost [1]
Approach | Average ISRN runtime (s) 32 CPUs |  | Total cost (CPUh) | 
 | Coarse | Fine | Coarse | Fine
HU-2EQN | 0.51 | 0.76 | 45.3 | 67.5
HyChem-2EQN | 4.8 | 9.1 | 427 | 809
HyChem-NAPS | 14.4 | 31.5 | 1,280 | 2,800
Polyhedral, 154 ISRs
Fine
Polyhedral, 78 ISRs
Coarse
complexity
[1] Gkantonas, S., Sirignano, M., Giusti, A., D’Anna, A., Mastorakos, E. (2020). Fuel 270, 117483.
Compare with detailed CFD with detailed chemistry: O(105)-O(106) CPUh
soot
gas
HU: Heidelberg Uni. dodecane scheme
HyChem: Jet-A1 Hybrid Chemistry
2EQN: Leung et al. two-equation model
NAPS: Napoli sectional model for C2H4

## Slide 8: Application 1: Kerosene combustor
LES-CMC
ISRN
LES-CMC
ISRN
OH
Temperature
Airblast atomisers (main+pilot)
Effusion cooling
Condition at pilot-only mode (low power)
Simulated with LES-CMC, two-equation soot model and a dodecane scheme
Big Optical Single Sector Combustor
ISR spacing
Polyhedral, 154 ISRs
[1] Giusti, A., Mastorakos, E., Hassa, C., Heinze, J., Magens, E. and Zedda, M. (2018). J. Eng. Gas. Power 140
[2] Gkantonas, S., Foale, J. M., Giusti, A., and Mastorakos, E. (2020). J. Eng. Gas. Power (press)

## Slide 9: Application 1: Kerosene combustor
EXP [1]
LES-CMC HU-2EQN
ISRN HU-2EQN
ISRN HyChem-NAPS
ISRN HyChem-2EQN
soot
gas
HU: Heidelberg Uni. dodecane scheme
HyChem: Jet-A1 Hybrid Chemistry
2EQN: Leung et al. two-equation model
NAPS: Napoli sectional model for C2H4
ISR spacing
Polyhedral, 154 ISRs

## Slide 10: Application 2: DLR burner
LES-CMC
EXP
ISRN
0.03 ppm
3 ppm
3 ppm
C2: Aramco mechanism (ethylene)
2EQN: two-equation soot model
ISR spacing
Polyhedral, 152 ISRs

## Slide 11: Application 3: Cambridge RQL burner
EXP
LES-CMC
ISRN
Dilution 40%
EXP
Dilution 0%
LES-CMC
ISRN
LES-CMC
ISRN
Burner-out
ISR spacing
Polyhedral, 32 ISRs
NAPS: - Napoli sectional model
- C2H4 oxidation chemistry

## Slide 12: Closure
Summary
Novel post-process approach for CFD
Simple, inexpensive and easily coupled with comprehensive soot models
Assessed and validated with detailed CFD of various combustors
Future steps
Parametric analyses and optimum solution strategy
More chemical mechanisms, soot models, more burners
Transient phenomena and multi-mode combustion

## Slide 13
Dr Mariano Sirignano & Prof. Andrea D’Anna (University of Naples)
Prof. Hai Wang (Stanford), Prof. Fokion Egolfopoulos (USC)
Acknowledgements
Contributors
Prof. Epaminondas Mastorakos
Dr Andrea Giusti
Miss Jenna M. Foale (Cambridge)
Thank you!