## Slide 1: Investigation of the effects of body forces on flame-turbulence interactions in turbulent premixed combustion
Arun Ravi Varma, Umair Ahmed, Nilanjan Chakraborty
School of Engineering, Newcastle University, Newcastle-Upon-Tyne, NE17RU, UK
UKCTRF Annual Meeting
16th September 2020

## Slide 2: Introduction: Motivation
Turbulent premixed flames are “ducted”  subjected to external pressure gradients
Considerable difference in density between unburned reactants and burned products  Buoyancy is expected influence flame characteristics
Last well-known study  Veynante and Poinsot1  Emphasis on scalar flux
Effects of body forces on statistical behaviour of flame surface density (FSD) and its evolution has not been analysed in existing literature
1 D. Veynante and T. Poinsot, J. Fluid Mech., vol. 353, pp. 83-114, 1997

## Slide 3: Introduction: Objectives
Investigate the effects of body force on:
  Flame wrinkling and flame brush thickness
  FSD statistics
  Terms of the FSD transport equation
Assess the performance of the existing closure models
Propose suitable modifications, wherever necessary, to capture the effects of the body force

## Slide 4: Mathematical Background
Momentum equation under the action of a body force:
is the source/sink term in the direction
stands for the inverse of Froude number-squared ()
is the Zel’dovich flame thickness
Positive  Unstable stratification
Negative  Stable stratification
Reactants
Products
x1
+g*
-g*
Flame

## Slide 5: Mathematical Background
Negligible in statistically planar flames in the context of RANS
Usually expressed in terms of the generalized FSD1
Beyond scope of present work
Progress variable
- suitable product mass fraction
Transport equation of Favre averaged progress variable :
1 M. Boger, D. Veynante, H. Boughanem, A. Trouvé, Proc. Combust. Inst. 27, pp. 917-925, 1998.

## Slide 6: Mathematical Background
Generalized FSD
Transport equation of generalized FSD:
  The terms , , , and are unclosed terms and need to be modelled

## Slide 7: Numerical Implementation
3D compressible DNS code SENGA+
Boundary conditions – NSCBC technique1
Turbulence field – pseudo spectral method of Rogallo2, Batchelor-Townsend energy spectrum3
values: 3.0, 5.0, 7.5, 10.0  Decaying turbulence
values: -3.12, -1.56, 0.0, 1.56, 3.12
Total of 20 simulation cases
Flame
Partially
non-reflecting
boundaries
Periodic
Periodic
z
x
y

## Slide 8: Numerical Implementation
Single-step Arrhenius type irreversible chemical reaction is considered
Standard value of parameters:
  Unity Lewis number
  Prandtl number = 0.7
  Zel’dovich number = 6.0
  Heat release parameter = 4.5 (methane flames preheated to 415K)
Simulation time > 3.0, where is the initial eddy turnover time (comparable to several previous studies)

## Slide 9: Results: Isosurfaces of
Flame wrinkling Flame brush thickness
Flame wrinkling Flame brush thickness
Consistent with previous findings of Veynante and Poinsot
 | = 3.0 | = 5.0 | =10.0
increases
increases
Instantaneous isosurfaces of

## Slide 10: Results: Normalized flame surface area and turbulent flame speed
= 3.0
= 5.0
= 7.5
= 10.0
is flame area projected in direction



## Slide 11: Results: Mean reaction rate closure
 | = 3.0 | = 5.0 | =10.0
Boger et al.1 
For unity Lewis number, according to several previous studies2,3
  is the density of the unburned gas
1 M. Boger, D. Veynante, H. Boughanem, A. Trouvé, Proc. Combust. Inst. 27, pp. 917-925, 1998.
2 R.S. Cant, S.B. Pope, K.N.C. Bray, Proc. Combust. Inst. 27, 809-815, 1990.
3 S. Candel, V. Venante, F. Lacas, E. Maistret, N. Darabhia, T. Poinsot, Recent Advances in Combustion Modelling, World Scientific, Singapore, 1990, pp. 19-64, 1990.
DNS data (solid line) and predictions of the model (dotted line)

## Slide 12: Results: Modelling of the turbulent transport term
 | = 3.0 | = 5.0 | =10.0
Modelling of is dependent on the modelling of the turbulent flux of generalized FSD
Model proposed by Chakraborty and Cant1
1 N. Chakraborty, R.S. Cant, Phys. Fluids 21 (2009) 035110, 1–11.
DNS data (solid line) and predictions of the model (dotted line)

## Slide 13: Results: Modelling of the combined term
Model1,2 for
  =
Satisfactorily predicts the combined propagation and curvature term
 | = 3.0 | = 5.0 | =10.0
DNS data (solid line) and predictions of the model (dotted line)
1 I. Hun, K.Y. Huh, Combust. Flame 152, 194-205, 2008.
2 N. Chakraborty, R.S. Cant, Combust. Flame 158, 1768-1787, 2011

## Slide 14: Results: Modelling the strain rate term
Existing models:
  CPB model1 (dotted lines) – based on the Kolmogorov time scale
  CFM model2,3 (dashed lines) – based on integral time scale
  DNS data (solid lines)
not satisfactorily captured by the existing models
Alternative model proposed
Predictions of the alternative model for (line with circles)
DNS data (solid lines)
CPB model (dotted lines)
CFM model (dashed lines)
Proposed model (lines with circles)
1 R.S. Cant, S.B. Pope, K.N.C. Bray, Proc. Combust. Inst. 27, 809-815, 1990.
2 D. Veynante, J. Piana, J.M. Duclos, C. Martel, Proc. Combust. Inst. 26 pp. 413–420, 1996.
3 S. Candel, V. Venante, F. Lacas, E. Maistret, N. Darabhia, T. Poinsot, Recent Advances in Combustion Modelling, World Scientific, Singapore, 1990, pp. 19-64, 1990.

## Slide 15: Results: Alternative model for
1
2
3
Based on the alignment of with the local fluctuating strain rates1,2
The proposed model for the term is given by:
and  contributions of the dilatation rate
and  normal strain rate contribution
Model parameters  and  functions of (Froude number)

## Slide 16: Conclusions
The effects of body force on the statistical behaviours of FSD and its transport have been evaluated using a DNS database of three-dimensional statistically planar turbulent premixed flames using the decaying turbulence approach.
  An unstable (stable) density stratification promotes (weakens) flame wrinkling
  Existing models satisfactorily capture and ()
  Alternative model for
  Effects of body force weakens with increasing turbulence intensity
where

## Slide 17: Future work
Effects of body force  forced turbulence approach.
A bandwidth-filtered forcing strategy1,2  maintain the turbulence level on the unburned gas side.

## Slide 18: Acknowledgements
The computational support of Rocket, Cirrus and ARCHER are gratefully acknowledged.
Time usage on ARCHER (approx. kAU): 6,000 kAU